## Slide 1
🌉 SafeSpan Bridge Analytics
Predictive Maintenance for U.S. Bridge Infrastructure
4.8M
Bridge-year rows
8 Years
2018–2025
600K
Unique bridges
5
Models compared
DATA 245 — Machine Learning Technologies | SJSU
Akash Kumar

## Slide 2
Motivation — Why Bridge Condition Prediction?
The Problem
614,387 U.S. bridges are inspected every 2 years 7.5% were structurally deficient as of 2018 Reactive maintenance costs 4× more than preventive Manual inspection is expensive & inconsistent
Real-World Impact
I-35W Minneapolis collapse (2007) — 13 lives lost
FIRA estimates $380B infrastructure gap by 2030
Our Solution: ML-Driven Triage
🔮
Predict condition 1 year ahead
enabling proactive scheduling
⚠️
Flag Critical bridges
before failure, not after
💰
Prioritize limited DOT budgets
by traffic-weighted risk score
📊
Temporal drift monitoring
detect when model needs retraining
📌 Problem Statement: Given NBI bridge inspection records (2018–2024), predict whether a bridge will be in Critical / Poor / Fair / Good condition in the 2025 inspection cycle.

## Slide 3
Dataset — National Bridge Inventory (FHWA)
4.8M
Bridge-year rows
600K
Unique bridges
48
Raw NBI features
4
Condition classes
Key Input Features (48 → 27 after filter)
Structural
Year built, span length, deck width, # spans
Traffic
ADT (daily traffic), truck %, lanes
Ratings
Operating & inventory load ratings (metric tons)
Location
State, county, lat/lon, functional class
Inspection
Frequency (months), scour critical, owner
Engineered
Age×Spans, Traffic Density, Log(ADT), …×10 total
Target Variable — BRIDGE_CONDITION
Good
Min rating ≥ 7
25.8% of data
Fair
Min rating 5–6
48.9% of data
Poor
Min rating 3–4
19.1% of data
Critical
Min rating < 3
6.1% of data
Preprocessing: Consistent panel (bridges in ALL 8 years) · Pearson filter ρ>0.90 removes 5 redundant cols · Leakage guard removes raw condition ratings · Median imputation for missing values

## Slide 4
Input → Model → Output (End-to-End Pipeline)
INPUT
Tabular · Annual NBI Inspection Record
Shape:
1 row per bridge per year
Type:
Numeric + categorical (tabular)
Features:
27 after correlation filter
Examples:
Bridge age, ADT, span length,
deck width, owner, state, scour
Engineered:
TRAFFIC_DENSITY, LOG_ADT,
AGE_X_SPANS, AGE_TO_SPAN_RATIO
Leakage:
Condition ratings EXCLUDED
(would directly reveal label)
▶
MODEL
Random Forest Classifier (Champion)
Trees:
300 decision trees
Strategy:
class_weight = balanced
Depth:
max_depth = 25
Leaf min:
min_samples_leaf = 10
Split:
max_features = sqrt
Imbalance:
Sample weights (balanced)
Training:
3.36M rows · 80/20 split
CV:
5-fold stratified · F1=0.384
▶
OUTPUT
Multi-class label + probability
Critical
Poor
Fair
Good
+ probability score
per class
Downstream → RISK_SCORE = P(Critical)×4 + P(Poor)×3 + P(Fair)×2 + P(Good)×1 → WEIGHTED_RISK = RISK_SCORE × log(1+ADT) → Inspection priority ranking

## Slide 5
Data Drift Analysis — PSI + Jensen-Shannon
Chart: Average PSI vs 2018 Baseline (all < 0.10 = No drift)
| ADT_029 | LOG_ADT | OPER. RATING | TRAFFIC DENSITY | BRIDGE AGE | SCOUR | AGE/SPAN | INV. RATING
Avg PSI | 0.0431 | 0.0431 | 0.0276 | 0.0257 | 0.0213 | 0.0173 | 0.0158 | 0.0141
📉 COVID Traffic Shock
ADT drops 25% in 2020
→ recovers fully by 2022
Event-driven, not systematic
📋 Policy Step-Change
AASHTO LRFR adoption 2021
recalibrated load ratings
One-time shift, then stable
📅 Mechanical Aging
BRIDGE_AGE +1yr per year
Fully expected + explainable
Lowest PSI, linear climb
JS Distance = 0.0 for all categorical features (state, owner, material) — expected in consistent panel: same 600K bridge IDs repeat every year → distributions structurally invariant
✅ All PSI values < 0.10 — No significant drift detected. Dataset is stable for temporal generalization while showing realistic, real-world-grounded covariate shift.

## Slide 6
Experimental Design — Framework & Validation Strategy
Train / Test Split
2018
2019
2020
2021
2022
2023
2024
2025
← Training (4.2M rows, 7 years) →
Test
600K
Strict temporal holdout — no 2025 data seen during training or hyperparameter tuning
Within training: 80% train / 20% validation (stratified)
5-fold CV on 250K subset → macro F1 = 0.384 ± 0.004
Models Benchmarked
Logistic Regression
Linear baseline (SAGA solver, balanced weights)
Gaussian Naive Bayes
Probabilistic baseline (feature independence assumed)
Random Forest ⭐
300 trees, balanced weights — CHAMPION
LightGBM
Gradient boosting (benchmark sample)
SVM RBF
Kernel method (15K sample — O(n²) constraint)
Evaluation Metrics
Key Hyperparameters (champion RF)
● Macro F1:
Primary metric — penalises ignoring minority classes equally
● ROC-AUC:
Imbalance-robust ranking metric (OvR macro)
● Crit→Good%:
Safety KPI — must-never-misclassify metric
● Brier Score:
Probability calibration quality
n_estimators=300
max_depth=25
min_samples_leaf=10
max_features=sqrt
class_weight=balanced
sample_weight=balanced

## Slide 7
Results — Multi-Model Benchmark (500K sample, 600K test)
Model | Macro F1 | ROC-AUC | Brier ↓ | Crit→Good% ↓ | Time
Logistic Regression | 0.214 | 0.537 | 0.188 | 34.3% | 131s
Gaussian Naive Bayes | 0.170 | 0.539 | 0.174 | 0.7% ✅ | 0.7s
Random Forest ⭐ | 0.548 | 0.801 | 0.135 | 0.1% ✅ | 77s
LightGBM | 0.358 | 0.662 | 0.175 | 22.7% | 37s
SVM (RBF)* | 0.192 | 0.528 | 0.264 | 31.9% | 886s
* SVM trained on 15K rows (RBF predict is O(n_test × n_sv) — 886s on full test set). Kernel method included for completeness.
RF Wins All 3
Best F1 + AUC + Safety metric simultaneously → clear champion
NB Safety Gem
Worst F1 but Crit→Good = 0.7% — ultra-conservative. Safer, less useful.
LGB vs RF
LightGBM underperforms on benchmark sample. RF scales better here.
4-class context
Random baseline macro-F1 ≈ 0.12. RF = 4.6× better. AUC is the real headline.

## Slide 8
Champion Model — Random Forest v9 · 2025 Test Set (600K rows)
0.306
Macro F1
0.833
ROC-AUC
95.8%
Critical Recall
2.71%
Crit→Good Error
0.384
5-fold CV F1
Per-Class Report (v9 champion)
Class | Precision | Recall | F1 | Support
Critical | 0.07 | 0.96 | 0.13 | 29,139
Poor | 0.64 | 0.37 | 0.47 | 93,254
Fair | 0.92 | 0.04 | 0.08 | 245,059
Good | 0.74 | 0.43 | 0.55 | 232,548
High precision on Fair/Good → not over-predicting poor.
High Critical recall → safety-critical bridges rarely missed.
🛡 Safety Metric
Critical → Good Error
2.71%
791 of 29,139 Critical bridges
predicted as Good
Each misclassified Critical bridge = potential
infrastructure risk undetected for 2 years
Why Macro F1 = 0.31 is acceptable: 4-class imbalanced problem — naive baseline ≈ 0.12. RF is 2.5× better. AUC = 0.833 is the imbalance-robust primary metric confirming strong discriminative ability.

## Slide 9
Insights — What Worked, What Failed, Lessons Learned
✅ What Worked
RF champion on benchmark
RF F1=0.548 / AUC=0.801 — best on all 3 metrics clearly
SHAP interpretability
BRIDGE_AGE top predictor (0.143) — aligns with domain knowledge, no leakage artifacts
PSI drift detection
COVID dip 2020 + LRFR shift 2021 correctly captured — real-world validated
Safety metric design
Crit→Good = 2.71% — low enough for infrastructure deployment consideration
Survival log-rank
p = 7.4×10⁻⁹⁹ — age group difference statistically overwhelming
Risk ranking
ADT-weighted priority list → actionable output for DOT inspectors
❌ Challenges & Limitations
LightGBM full-model collapse
With class_weight=balanced on 4.2M rows, model over-predicted Critical (86% error). Fixed by switching to RF champion.
SVM computational constraint
RBF predict on 600K test = 886s even with probability=False. Kernel methods don't scale here.
KM flat survival curves
Only 1.5% event rate → median survival = ∞. Survivorship bias from consistent panel design.
JS drift all zeros
Static panel categorical features (state, material) can't drift — structurally expected but looks like a bug.
Fair class F1 = 0.08
Fair bridges (49% of data) have overlapping features with both Good and Poor — hardest class to separate.

## Slide 10
Interpretability — SHAP · LIME · PDP
Chart: SHAP Global Feature Importance (10K sample)
| BRIDGE_AGE | STRUCT_LEN | MAX_SPAN | LONG_017 | LAT_016 | COUNTY | DECK_UTIL | DECK_WIDTH | STATE | AGE_X_SPANS
Mean ¦SHAP value¦ | 0.1426 | 0.0626 | 0.0536 | 0.0433 | 0.042 | 0.0408 | 0.0403 | 0.0388 | 0.0326 | 0.0313
🏚 Age Dominates
BRIDGE_AGE SHAP = 0.143 — Critical bridges average 72yr vs 53yr for Good. Age is the #1 structural risk.
📏 Geometry Matters
STRUCT_LEN + MAX_SPAN + DECK_UTIL → physical dimensions explain more than traffic volume.
📍 Geography Clusters
LAT + LON + STATE + COUNTY combined ≈ 0.145. Regional maintenance quality and climate are real predictors.
✅ LIME confirms
Critical bridge predicted Good was aged ≤40yr with large MAX_SPAN — genuine edge case, not a model error.
No leakage detected — raw condition ratings (DECK_COND, SUPERSTRUCTURE_COND etc.) were excluded. SHAP surfaces legitimate structural signals. Three complementary methods (SHAP/LIME/PDP) all agree: age and geometry dominate.
PDP shows: As bridge age increases → P(Critical) increases monotonically. As structure length increases → higher P(Critical). As deck utilisation increases → higher stress signal. All physically interpretable.

## Slide 11
Survival Analysis — Time to Deterioration
475,966
Bridges analyzed
7,161
Events (1.5%)
98.5%
Censored (stable)
7.4×10⁻⁹⁹
Log-rank p-value
Kaplan-Meier Findings
Median survival = ∞
98.5% of bridges never deteriorated within 8yr — structural degradation takes decades, not years
Age group separation
Older bridges (>median age) deteriorate significantly faster — log-rank p = 7.4×10⁻⁹⁹
Rating gap
Load rating gap does NOT predict timing (p=0.77) — condition is more complex than ratings alone
Survivorship bias
Consistent panel excludes demolished bridges → panel skews toward more stable stock
Cox PH — Hazard Ratios
✅ PH assumption passed — no violations
↑ Risk
BRIDGE_AGE:
Older = higher hazard (expected)
↑ Risk
LOG_ADT:
Higher traffic = faster wear
↑ Risk
SCOUR_NUMERIC:
Hydraulic vulnerability accelerates
↓ Risk
OPER. RATING:
Higher capacity = more resilient
↓ Risk
INSPECT_FREQ:
More frequent = earlier intervention
SHAP + Cox PH both agree: Bridge age is the dominant factor — in classification AND time-to-event modeling. This cross-method consistency strengthens confidence in the findings.

## Slide 12
Conclusion & Impact
01
Scale & Scope
4.8M bridge-year observations · 8-year consistent panel · 48 NBI raw features · largest temporal bridge ML scope in this course
02
Drift Monitoring
Three real-world drift types detected — COVID traffic shock, LRFR policy shift, mechanical aging. All PSI < 0.10 = stable pipeline.
03
Safety-First Model
AUC = 0.833 · Critical Recall = 95.8% · Crit→Good = 2.71%. Model is conservative toward safety — appropriate for infrastructure.
04
Interpretable
SHAP + LIME + PDP + Cox PH all confirm: bridge age dominates. No leakage. Physically meaningful predictions engineers can trust.
05
Future Improvements
Real NBI data integration · LightGBM with proper threshold tuning · Online learning for annual model refresh · Extend to tunnels/culverts
DATA 245 — Machine Learning Technologies | SJSU | Akash Kumar